## Slide 1
PHISON • AI MEMORY SYSTEMS
Phison aiDAPTIV
Flash as a managed AI memory tier
Current name: Pascari aiDAPTIV = Middleware + Cache Memory
SSD / NAND
retained capacity
System DRAM
staging / warm state
GPU VRAM
active working set
GPU compute
tensor cores execute
SYSTEM ROLE
Breaks the memory-capacity wall before compute is exhausted.
Keeps active state near compute; retains colder state below.
Supports documented inference and fine-tuning integrations.
Adds capacity—not tensor compute or HBM-class latency.
01
Notes: Current Phison materials use Pascari aiDAPTIV as the umbrella name. The public architecture is middleware plus a dedicated flash capacity tier across GPU/unified memory, system memory, and cache memory. SSD does not replace GPU compute.
[Sources]
https://www.phisonenterprise.com/pascari-aidaptiv/
https://www.phisonenterprise.com/how-pascari-aidaptiv-works/
https://www.phison.com/phison-rescales-local-ai-inferencing-with-flash-memory-expansion-2/

## Slide 2
WHY A NEW MEMORY HIERARCHY
02
Capacity expands as memory gets slower
Phison aiDAPTIV technical architecture • Sources and claim boundaries in speaker notes
Representative—not apples-to-apples. Actual bandwidth and latency depend on platform topology, channel count, queueing, and access pattern.
Tier
Capacity
Peak bandwidth
Latency
Cost / GB
Persistence
GPU HBM / VRAM
10s–100s GB / GPU
TB/s class
H100: 3.35 TB/s
Lowest
Highest
No
CPU DRAM
100s GB–TB / node
10s–100s GB/s
platform aggregate
Low
Medium
No
NVMe SSD
TBs per drive
GB/s class
E28: up to 14.5 GB/s
Highest
Lowest
Yes
Why LLMs spill
weights + growing KV cache + activations + gradients + optimizer state + checkpoints can exceed the fast tier
Notes: The table is a representative engineering hierarchy, not a benchmark comparison. NVIDIA publishes 80 GB and 3.35 TB/s for H100 SXM. Phison publishes up to 14.5 GB/s sequential throughput for the E28 controller. DRAM is intentionally expressed as a range because channel count and CPU platform dominate.
[Sources]
https://www.nvidia.com/en-us/data-center/h100/
https://www.phison.com/ces-2025-phison-unveils-lightning-fast-gen5-storage-expanding-suite-of-high-performance-solutions/
https://www.phisonenterprise.com/pascari-aidaptiv/

## Slide 3
AIDAPTIV SYSTEM ARCHITECTURE
03
aiDAPTIV manages a three-tier working set
Phison aiDAPTIV technical architecture • Sources and claim boundaries in speaker notes
CONFIRMED BY PHISON
aiDAPTIV Middleware orchestrates AI data across GPU, DRAM, and flash.
Cache Memory retains eligible less-active KV, experts, model, or training state.
Discrete-GPU and unified-memory system patterns are supported where integrated.
Placement varies by runtime, model, sequence length, batch, and hardware.
GPU / unified memory
active layers • KV • experts
System DRAM
prefetched / near-term / intermediate state
aiDAPTIV Cache Memory
retained colder state • dedicated NVMe tier
aiDAPTIV
Middleware
AI-aware
placement
and movement
runtime-specific
NOT PUBLICLY SPECIFIED
eviction granularity • queue policy • prefetch algorithm • direct-storage path. No public GPUDirect Storage claim; host staging is the safe default model.
Notes: Solid architecture elements are directly documented. The lower callout lists proprietary/undocumented details. Public Phison material does not document GPUDirect Storage, a direct GPU-to-SSD DMA contract, exact cache granularity, or eviction policy, so the deck does not claim those mechanisms.
[Sources]
https://www.phisonenterprise.com/how-pascari-aidaptiv-works/
https://www.phisonenterprise.com/pascari-aidaptiv/
https://github.com/aiDAPTIV-Phison/aiDAPTIV

## Slide 4
AIDAPTIV FOR LLM INFERENCE
04
Retained AI state avoids repeated work
Phison aiDAPTIV technical architecture • Sources and claim boundaries in speaker notes
DOCUMENTED INFERENCE MODES
Cache Memory
less-active KV • expert pool
DRAM
staging / warm
VRAM
active state
Tensor cores
prefill / decode
KV extension + prefix reuse
Retain eligible KV state beyond the fast tier.
Reuse requires identical tokens from the prompt start.
Best: stable system prompts, documents, RAG blocks, agents.
Dynamic MoE: expert locality
Retain the full expert pool in cache memory.
Bring selected experts toward compute as routed.
Stalls grow when expert locality is poor or choices vary rapidly.
ENGINEERING PATTERN—VERIFY RUNTIME
Dense layer-on-demand streaming with asynchronous prefetch is common in NVMe offload systems, but current public Phison pages emphasize KV reuse and MoE; Link 3 carries inference features.
Notes: Confirmed current inference mechanisms are KV-cache extension/reuse and Dynamic MoE. The dense layer-streaming statement is deliberately labeled as an industry pattern, not a documented proprietary Phison scheduler. The official GitHub separates Link 2 fine-tuning focus from Link 3 inference features.
[Sources]
https://www.phisonenterprise.com/kv-cache-extension-reuse/
https://www.phisonenterprise.com/dynamic-moe/
https://github.com/aiDAPTIV-Phison/aiDAPTIV
https://www.deepspeed.ai/2022/09/09/zero-inference.html

## Slide 5
AIDAPTIV FOR FINE-TUNING
05
Elastic Fine-Tuning is a core capability
Phison aiDAPTIV technical architecture • Sources and claim boundaries in speaker notes
OFFICIAL LINK 2 CAPABILITIES
aiDAPTIV Cache Memory
• model / training state
• optimizer state*
• dataset + checkpoints*
• activations*
System DRAM
staging • CPU Adam • near-term
GPU VRAM
current layers • grads • activations
forward • backward • update
aiDAPTIVLink 2
LoRA and full-parameter fine-tuning
CPU Adam optimizer support
1 / 2 / 4 / 8 GPUs and multi-node
Vision-language model support
SSD-based GPU-memory offload
Linux runtime; PCIe topology matters
CLAIM BOUNDARY
*Training-state staging is confirmed; exact tensor placement is runtime-specific.
Notes: Fine-tuning support is explicit. The official repository lists LoRA and full-parameter fine-tuning, CPU Adam, multi-GPU/multi-node, VLM, and SSD-based GPU-memory offload. Current product pages discuss LoRA and QLoRA and state that exact placement varies by runtime and training method. The diagram avoids claiming that every optimizer/activation tensor is always placed on SSD.
[Sources]
https://www.phisonenterprise.com/elastic-fine-tuning/
https://github.com/aiDAPTIV-Phison/aiDAPTIV
https://www.phisonenterprise.com/how-pascari-aidaptiv-works/

## Slide 6
FINE-TUNING EXAMPLE
06
70B fine-tuning exposes the memory wall
Phison aiDAPTIV technical architecture • Sources and claim boundaries in speaker notes
FP16 weights alone: 70B parameters × 2 bytes ≈ 140 GB. Gradients, optimizer state, activations, and temporary buffers increase the live footprint.
Traditional fit strategy
Keep most training state in accelerator memory
Model weights
Gradients
Optimizer state
Activations / buffers
Result: multiple high-memory GPUs or OOM
aiDAPTIV placement strategy
Reserve fast memory for the current training working set
Hot — VRAM
layers / grads / activations
Warm — DRAM
prefetched / CPU-managed state
Cold — SSD cache
staged model or training state
Vendor guidance: 2 TB cache → up to 70B, 128 GB RAM. Validate per model/method.
Phison internal result
4× RTX 4090 • Llama 2 70B • 519→971 tokens/s (1.0→2.0/E28)
Vendor-reported; public methodology is incomplete—do not generalize.
Notes: The 140 GB FP16 weight figure is arithmetic, not a benchmark. Training-state footprint depends on precision, optimizer, LoRA/QLoRA/full tuning, checkpointing, batch, and sequence length. Phison's official GitHub publishes the 2 TB/up-to-70B/128 GB RAM sizing guidance. The 519-to-971 tokens/s number is a Phison internal comparison with incomplete public methodology and is labeled accordingly.
[Sources]
https://github.com/aiDAPTIV-Phison/aiDAPTIV
https://www.phison.com/phisons-worlds-first-6nm-ai-computing-ssd-solution-wins-computex-2025-best-choice-golden-award/
https://www.phisonenterprise.com/elastic-fine-tuning/

## Slide 7
AIDAPTIV VS DEEPSPEED ZERO
07
ZeRO schedules; aiDAPTIV engineers storage
Phison aiDAPTIV technical architecture • Sources and claim boundaries in speaker notes
AREA
DEEPSPEED ZERO
PASCARI aiDAPTIV
Primary unit
Software framework / runtime
Hardware + firmware + middleware platform
VRAM reduction
Sharding and offload
Workload-dependent tiering / retention
CPU / NVMe
CPU: Offload; NVMe: Infinity / Inference
DRAM + dedicated flash capacity tier
Inference
Layer streaming in ZeRO-Inference
KV reuse, Dynamic MoE; Link 3 inference
Fine-tuning
ZeRO-2/3, Offload, Infinity
Elastic FT; Link 2 LoRA/full FT/CPU Adam
Storage scope
Generic NVMe device and I/O stack
Controller + firmware + NAND + cache SSD
Relationship
Strategy can consume an NVMe tier
Optimized tier can make offload practical
Not necessarily competitors: no public official Phison–DeepSpeed integration was found; this is a conceptual layer comparison.
Notes: DeepSpeed descriptions come from its official tutorials. aiDAPTIV descriptions come from Phison's current product pages and official GitHub. No official integration between the two was identified in reviewed official materials as of 2026-08-29, so the relationship is explicitly conceptual.
[Sources]
https://www.deepspeed.ai/tutorials/zero/
https://www.deepspeed.ai/tutorials/zero-offload/
https://www.deepspeed.ai/2022/09/09/zero-inference.html
https://www.phisonenterprise.com/how-pascari-aidaptiv-works/
https://github.com/aiDAPTIV-Phison/aiDAPTIV

## Slide 8
ZERO TECHNICAL COMPARISON
08
ZeRO separates sharding from offload
Phison aiDAPTIV technical architecture • Sources and claim boundaries in speaker notes
TRAINING MEMORY STATES
Stage 1
optimizer states
Stage 2
+ gradients
Stage 3
+ parameters
ZeRO-Offload
optimizer + compute
→ CPU DRAM
NVME EXTENSIONS
ZeRO-Infinity — training
ZeRO-3 + CPU/NVMe offload engine
model states and activations can leave GPU memory
bandwidth-centric partitioning and overlap are essential
ZeRO-Inference — inference
host weights in CPU or NVMe
stream layer-by-layer into GPU
prefetch and overlap; optimized for throughput-oriented batches
Conceptual fit: ZeRO schedules placement; aiDAPTIV engineers the flash tier. No official integration is claimed.
Notes: Stage definitions and offload behavior are from DeepSpeed's official tutorials. ZeRO-Inference explicitly streams layers from CPU/NVMe and uses prefetching; it is positioned for throughput-oriented inference. aiDAPTIV is compared as a platform layer only, without claiming official integration.
[Sources]
https://www.deepspeed.ai/tutorials/zero/
https://www.deepspeed.ai/tutorials/zero-offload/
https://www.deepspeed.ai/2022/09/09/zero-inference.html
https://www.microsoft.com/en-us/research/blog/zero-infinity-and-deepspeed-unlocking-unprecedented-model-scale-for-deep-learning-training/

## Slide 9
WHY SSD-STACK OWNERSHIP MATTERS
09
SSDs need predictable behavior under AI load
Phison aiDAPTIV technical architecture • Sources and claim boundaries in speaker notes
AI tiering repeatedly retains, updates, evicts, restores, and overwrites state—unlike bursty desktop storage.
Workload pressure
Controller / firmware lever
System effect
large sequential tensor reads
channels, queueing, prefetch friendliness
sustained feed rate
concurrent reads + writes
QoS and workload contention
tail-latency consistency
checkpoint / cache churn
wear leveling, NAND correction, endurance
predictable service life
long transfers at Gen5 rates
thermal and power management
avoid throttling cliffs
recovery and data placement
firmware policy + media management
durability and repeatability
Current Cache Memory roadmap
AI100E PCIe 4.0 • AI200E / AI250E / AI20E PCIe 5.0 • AI20EH hybrid storage + cache
Product-level endurance, capacity, and warranty vary by SKU; verify the deployed configuration.
Notes: Phison's current Cache Memory page explicitly identifies sustained writes, latency variation, wear management, data placement, recovery behavior, and workload contention as controller/firmware concerns. The product-family roadmap is copied from that page. E28 bandwidth is not used as a guarantee for every aiDAPTIV cache SKU.
[Sources]
https://www.phisonenterprise.com/aidaptiv-cache-memory/
https://www.phison.com/ces-2025-phison-unveils-lightning-fast-gen5-storage-expanding-suite-of-high-performance-solutions/

## Slide 10
END-TO-END EXECUTION EXAMPLE
10
The target is to hide I/O behind useful GPU work
Phison aiDAPTIV technical architecture • Sources and claim boundaries in speaker notes
GENERAL IMPLEMENTATION PATTERN
The tiering principle is confirmed; the exact scheduler and timing below are illustrative, not a published Phison contract.
1
retain
state on SSD
2
prefetch
SSD → DRAM
3
promote
DRAM → VRAM
4
compute
forward / backward
5
evict
state → lower tier
6
overlap
prefetch ahead
TIME →
GPU
SSD / PCIe
Compute N
Compute O
Compute P
Compute Q
Prefetch O
Prefetch P
Prefetch Q
If transfer time exceeds available compute overlap, GPU utilization collapses; topology, batch/sequence, locality, and queue behavior determine the stall.
Notes: The six-step flow and overlap timeline are a general heterogeneous-memory implementation pattern. Phison confirms the three-tier retention model and workload-specific state movement but does not publicly specify this exact prefetch scheduler or timeline.
[Sources]
https://www.phisonenterprise.com/how-pascari-aidaptiv-works/
https://www.deepspeed.ai/2022/09/09/zero-inference.html
https://www.microsoft.com/en-us/research/blog/zero-infinity-and-deepspeed-unlocking-unprecedented-model-scale-for-deep-learning-training/

## Slide 11
BENEFITS AND LIMITATIONS
11
aiDAPTIV adds capacity—with hard I/O limits
Phison aiDAPTIV technical architecture • Sources and claim boundaries in speaker notes
Where it helps
larger models than GPU VRAM alone permits
long-lived or reusable context and KV state
sparse MoE models with useful expert locality
memory-constrained LoRA, QLoRA, or full fine-tuning
private on-prem deployments with fixed hardware
Where it can hurt
very low-latency or small-batch token generation
models already resident in VRAM
poor prefetch, expert locality, or prefix reuse
oversubscribed PCIe roots or NUMA-unaware placement
heavy write churn without endurance / thermal headroom
Measure TTFT • inter-token latency • throughput • GPU idle • PCIe utilization • SSD P99 latency • temperature • write amplification
Notes: This is a balanced engineering assessment synthesized from Phison's own capacity/tradeoff statements, KV/MoE suitability guidance, cache-memory endurance discussion, and DeepSpeed's throughput-versus-latency guidance for NVMe streaming.
[Sources]
https://www.phisonenterprise.com/how-pascari-aidaptiv-works/
https://www.phisonenterprise.com/kv-cache-extension-reuse/
https://www.phisonenterprise.com/dynamic-moe/
https://www.phisonenterprise.com/aidaptiv-cache-memory/
https://www.deepspeed.ai/2022/09/09/zero-inference.html

## Slide 12
KEY TAKEAWAYS
12
Five interview-ready conclusions
Phison aiDAPTIV technical architecture • Sources and claim boundaries in speaker notes
01
aiDAPTIV makes flash an active, managed AI memory tier—not a substitute for GPU compute.
02
Inference value is concrete: retain/reuse KV state and exploit sparse MoE expert locality.
03
Fine-tuning is equally central: Elastic Fine-Tuning and Link 2 support SSD offload, LoRA/full FT, CPU Adam, and scale-out.
04
ZeRO and aiDAPTIV operate at different layers: software placement strategy versus an integrated SSD/NAND/middleware platform.
05
Success depends on hiding transfer, preserving locality, and engineering the PCIe + SSD path for sustained, predictable service.
Ask Phison: runtime matrix? state-placement policy? direct-storage roadmap? qualification method? endurance telemetry?
Notes: Closing synthesis. The questions at the bottom convert the public-document gaps into productive engineering discussion topics: runtime matrix, placement policy, direct-path plans, qualification methodology, and endurance observability.
[Sources]
https://www.phisonenterprise.com/pascari-aidaptiv/
https://www.phisonenterprise.com/how-pascari-aidaptiv-works/
https://github.com/aiDAPTIV-Phison/aiDAPTIV
https://www.deepspeed.ai/tutorials/zero/